## Slide 1: VHDL design and FPLD implementation for Silicon Track Card
Presentation by Shweta Lolage
In partial fulfillment of the
requirements for the degree
of Masters Of Science

## Slide 2: Contents
D0 experiment
D0 detector
The project
Choice of VHDL
FPLDs
The electronics
Main data path
Individual modules
Simulation results
MATLAB model
Design approaches
Conclusion
Future work

## Slide 3: D0 experiment
DZERO Experiment is conducted at Fermi National Acceleration Laboratory.
In the D0 experiment a proton – anti proton at very high energy are made to collide in the TeVatron accelerator. This is carried out to find out about the smallest particles - quarks emitted in the collision.
The TeVatron Accelerator

## Slide 4: D0 experiment (continued)
This experiment is currently undergoing a significant upgrade of its detector electronics.
D0 trigger electronics has three levels:
Level_1
Level_2
Level_3

## Slide 5: The project
Part of L2STT, which is part of Level_2 trigger electronics of the D0 detector.
To implement the design logic of main data path of a single channel of Silicon Track Card (STC).
The design logic is implemented using the VHSIC Hardware Description Language (VHDL).

## Slide 6: Choice of VHDL
D0 Detector gives a large amount of data.
Processing time - few micro-seconds.
VHDL is used to implement the design in hardware example Field Programmable Logic Devices (FPLDs).
VHDL is independent of technology

## Slide 7: Field Programmable Logic Devices (FPLDs)
High speed, high performance logic gates
The logic can be downloaded onto device when in field
Using VHDL, very complex logic can be easily developed and mapped onto the device with synthesis tool

## Slide 8: FPLDs (continued)
Synthesis tools available
MAXPLUS – II
Quartus
Foundation
Synopsis

## Slide 9: Sample VHDL code
library altera;
use altera.maxplus2.all;
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_arith.all;
entity comparator is
port (centroid : in unsigned (10 downto 0);
roaddata : in unsigned (10 downto 0);
compare : out std_logic
);
end entity comparator;
architecture behavior of comparator is
constant zero11 :unsigned ( 10 downto 0) := "00000000000";
begin
process(roaddata,centroid)
begin
compare <= '0';
if(roaddata /= zero11 and centroid /= zero11 ) then
if (roaddata > centroid ) then
compare <= '1';
else
compare <= '0';
end if;
else
compare <= '0';
end if;
end process;
end architecture

## Slide 10: The L2STT flowchart
D0 internal presentation

## Slide 11: Block diagram of the STC data path
To L3 Buffers
Control Lines Main Control
Data Lines
Handshake Signals
Control Lines
Strip Reader
VTM Data
Centroid
Finder
Down -loaded Parameters
Data from the main controller
Centroids
Roads from FRC
Hit Filter
Hits
Z-centroids

## Slide 12: Downloaded parameters and monitoring data
Data from Main Control Module
Road data LUT
Hit Filter
Monitoring Data
Counters from Strip Reader and Centroid Finder
Monitoring data to Main Control Module
Gain Offset LUT
Strip reader
Test data LUT
Miscellaneous Data
Centroid Finder
Memory allotted to Memory space Memory address
Monitor space 1K X 32 0000 – 03FF
Miscellaneous 1K X 32 0400 – 07FF
Gain Offset LUT 4K X 8 0800 – 17FF
Test data LUT 1K (default) 1800 – 1BFF
(required) 256 X 18
Empty Space 1C00 – 3FFF
Road data LUT 16 K X 22 4000 – 7FFF

## Slide 13: Example data stream
AA 77 81 00 40 03 41 0D 42 06 50 06 51 10 52 07 6B 03 6C 04 6D 05 6E 04 6F 03 82 00 77 07 78 06 79 07 C0 C0
SEQ_ID
HDI_ID
CHIP_ID
BYTE OF ZEROS
STRIP NUMBER
DATA VALUE
END OF EVENT

## Slide 14: Strip Reader
Hand shaking signals
Data stream
SMT
Data filter
SMT Data
F
I
F
O
Test Data
From Memory
SMT
Test Select
To L3 Buffers
Strip Reader Control
F
I
F
O
To
Centroid Finder
Data
From Memory
8
18
18
18
23
17..16
15..8
7..0
error bits
higher byte
lower byte
22..21
20
19
18..11
10..7
6..0
Data type
New data bit
End of data
Data
Chip Id
Strip number

## Slide 15: Centroid Finder
From
Strip Reader
Data stream
Control signal
Handshaking signals
Cluster
Finder
Centroid Calculator
Data from
Memory
F
I
F
O
To
Hit Filter
To
L3 Buffer
To
Hit Filter
To
L3 Buffer
23
17
Data stream from Centroid Calculator to Hit Filter
16..15
14..13
12..2
1..0
Data type
Pulse Area
Centriod
Precision bits

## Slide 16: Clustering algorithm example
Centroid
Clusters
Strips
Pulse height
Threshold_1
Threshold_2
1 2 3 4 5 6 7 8 9 10 11 12

## Slide 17: Centroid Calculator
Centroid for three-strip cluster
Centroid for five-strip cluster
Pulse area of the cluster
Pulse area | Sum = D1 + D2 + D3 + D4 + D5
00 | < Pulse_Threshold_1
01 | Pulse_Threshold_1, Pulse_Threshold_2 
10 |  Pulse_Threshold_2, Pulse_Threshold_3 
11 |  Pulse_Threshold_3
Data stream from Cluster Finder constitutes five 8-bit data words and one 11-bit address

## Slide 18: Hit filter
32
31..26
25..24
23..16
15..13
12...2
1..0
Track No.
Pulse Area
SEQ_ID
HDI_ID
Centroid
Precision bits
22
11
32
Hit Register module
Comparator
module
Hits
Hit Format module
To L3 buffer
Data stream
Control signal
Hit interface module
Hit Readout module
Hit Filter Control module
Z-centroid module
Centroids from Centroid Finder
17
46

## Slide 19: Simulation of the design
A simulation of the design was done using MAXPLUS-II as the synthesis tool.
The test data based on previous studies was obtained from Boston University.
The test data was used to check the functionality of the design.

## Slide 20: Test data
AA 77 81 00 6B 03 6C 04 6D 05 6E 04 6F 03 C0 C0
SEQ_ID
HDI_ID
CHIP_ID
BYTE OF ZEROS
STRIP NUMBER
DATA VALUE
END OF EVENT

## Slide 21: Simulation result in MAXPLUS-II

## Slide 22: MATLAB Model
This model functionally emulates the VHDL model.
It was designed to check the functionality of the VHDL model.
Both the models agree on the result for the test data streams.

## Slide 23: Approaches to fit the design in minimum number of FPLDs
Different design approaches showed that
the synthesis tool first tries to fit the memory blocks and then the logic cells.
each memory assignment occupies more than one Embedded Array blocks, because of the word length
Thus the memories for downloaded parameters were allowed to be mapped in logic cells.
The overall design – Strip Reader, Centroid Finder, Hit Filter and the L3 buffers - was found to best fit in three FLEX 10KE FPLDs.

## Slide 24: Conclusion
The design is functionally correct, and successfully fits in three FLEX10KE FPLDs.
The first prototype using this design for the main data path is being built at Boston University.

## Slide 25: Further research
The design can be modified to fit into a larger FPLD to improve the timing of the logic.
New FPLDs such as APEX by ALTERA and VIRTEX by XILINX may be used.

## Slide 26: Acknowledgements
Dr. Reginald Perry.
Dr. Horst Wahl.
Dr. Simon Foo.
Dr. Bruce Harvey.
Department of Electrical and Computer Engineering, FAMU-FSU COE.
Department of Physics at FSU and BU.
National Science Foundation